## Slide 1
Karma-Based Credit Scheduler (KBCS)
A P4-Based Fairness Mechanism for Heterogeneous TCP Flows
Mid-Semester Project Presentation
Gaurav Jaiswal (IIT2023157) · Ishan Chadha (IIT2023158) · Sameer Prasad (IIT2023134)
Indian Institute of Information Technology, Allahabad
March 2026

## Slide 2
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
2/22
Presentation Outline
1
The Fairness Problem in Modern Networks
2
TCP CCA Families & Buffer Competition
3
Programmable Data Planes with P4
4
Baseline System: P4air — Architecture & Results
5
Our Proposal: KBCS — Core Idea & Algorithm
6
KBCS Architecture & Processing Pipeline
7
Implementation Status & Design Gaps
8
Experimental Evaluation & Metrics
9
Roadmap to End-Semester
10
Key Takeaways

## Slide 3
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
3/22
The Fairness Problem
Why do some TCP flows starve while others dominate?
Real networks carry diverse TCP algorithms simultaneously
  CUBIC, BBR, Vegas, Illinois — all competing for the same buffer
Aggressive senders fill buffers, delay-sensitive senders back off
  Result: unfair bandwidth distribution at bottleneck links
Traditional AQM (RED, CoDel) treats all flows identically
  Cannot distinguish the aggressor from the victim
Key Question:
  Can a programmable switch detect & correct this unfairness
  in real-time, without modifying the end hosts?
🏟 The Buffer Arena
CUBIC: "I'll fill the buffer until
packets drop — that's how
I find the link capacity."
BBR: "I'll estimate BDP and stay
below the queue limit."
Vegas: "Any RTT increase means
congestion — I'll back off."
→ Same buffer, conflicting strategies
→ CUBIC dominates every time

## Slide 4
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
4/22
TCP Congestion Control Families
Four families with fundamentally different strategies
CCA Family | Signal Used | Examples | Aggressiveness
Purely Loss-Based | Packet loss | CUBIC, Reno, BIC | Highest — fills buffer until loss
Loss-Delay Hybrid | Loss + RTT | Illinois, YeAH, Veno | Medium — delay as secondary signal
Delay-Based | RTT increase | Vegas, LoLa | Lowest — backs off at first sign
Model-Based | BDP estimation | BBR | Variable — periodic probing
⚡ Core Conflict
When loss-based and delay-based flows
share a FIFO queue, loss-based ALWAYS wins.
Loss-based needs losses to slow down.
Delay-based backs off before losses occur.
→ Fundamentally asymmetric competition.

## Slide 5
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
5/22
Bufferbloat & Why Traditional AQM Fails
The Bufferbloat Cascade
  CUBIC fills the shared buffer → queuing delay rises for ALL
  BBR sees inflated RTT → reduces pacing rate
  Vegas detects delay → backs off entirely → starvation
Why RED/CoDel Can't Help
  Flow-agnostic: same drop probability for all packets
  Drops a Vegas packet = punishes the victim
  Drops a CUBIC packet = exactly what CUBIC expects
What We Need Instead
  Behavior-aware differentiation at the switch
  Protect well-behaved flows, penalize aggressors
📊 Literature Evidence
Without CCA awareness:
Jain's FI as low as 0.18 – 0.49
(P4air paper, Turkovic & Kuipers 2021)
With CCA-aware scheduling:
Jain's FI improves to 0.87 – 0.96
→ Strong motivation for in-switch fairness

## Slide 6
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
6/22
P4 & Programmable Data Planes
Moving fairness logic INTO the switch
P4: Protocol-Independent Packet Processing
  Switch pipeline defined by the operator, not the vendor
  Parser → Ingress → Traffic Mgr → Egress → Deparser
Key P4 Capabilities We Leverage
  Registers: persistent per-flow state across packets
  Hash functions: CRC16 for flow identification
  Bit-shift ALU: efficient decay without floating point
  Priority queues: differentiated scheduling in BMv2
Our Environment
  BMv2 simple_switch + Mininet + P4_16
  Dumbbell topology: 10 Mbps bottleneck, 5ms delay
v1model Pipeline
┌─────────────────┐
│ Parser │
└────────┬─────────┘
↓
┌─────────────────┐
│ Ingress Control │ ← KBCS logic here
└────────┬─────────┘
↓
┌─────────────────┐
│ Traffic Manager │ ← Priority queues
└────────┬─────────┘
↓
┌─────────────────┐
│ Egress Control │
└─────────────────┘

## Slide 7
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
7/22
Related Work at a Glance
10 papers spanning 4 research areas
Research Area | Key Papers | What They Contribute
CCA-Aware Fairness | P4air, P4CCI, Real-Time CCA ID | In-switch flow classification & treatment
Buffer/Queue Mgmt | CCA-aware QM, P4 Buffer Mgmt | Programmable queue policies for fairness
Fair Queueing | PFQ (Proactive Fair Queueing) | Fairness + high utilization simultaneously
Network Telemetry | HINT (In-Band Telemetry) | P4-driven congestion feedback via INT
Multi-Agent CC | MARL-CC | RL-based cooperative fairness learning
P4 Frameworks | P5, P4-NEON | Event-driven & SDN-based P4 policies
Research Gap We Target
FIFO / RED / CoDel → too simple, flow-agnostic
P4air / P4CCI → effective but complex
(13+ registers, RTT estimation, recirculation)
KBCS targets the middle ground:
Behavior-aware + Implementation-simple
→ Only 2 registers per flow
→ No timer dependency

## Slide 8
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
8/22
Baseline: P4air Architecture
Three-module CCA-aware pipeline (Turkovic & Kuipers, 2021)
Module 1: Fingerprinting
• SYN-based RTT estimation
• Per-RTT packet count tracking
• Queue-depth growth streak analysis
• BBR bandwidth probing detection
Flow lifecycle:
Ant → Mice → Delay → Loss-Delay → Pure Loss
(+ Model-Based branch for BBR)
Module 2: Reallocation
• 8 hardware queues (Q0–Q7)
• Q0, Q1 reserved for short flows
• Q2–Q7 dynamically allocated
• Proportional to active flows per group
Boundaries l₁, l₂, l₃ updated
each RTT interval
Module 3: Apply Actions
When flow exceeds BDP fair share:
• Loss-based → DROP packet
• Delay-based → RECIRCULATE (delay)
• Model-based → HALVE TCP window
CCA-specific penalties = precise
but complex to implement
⚠ P4air in BMv2: 13+ registers per flow, RTT-dependent, recirculation-heavy

## Slide 9
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
9/22
P4air: Software Emulation Challenges
Why complexity hurts in BMv2
1. CPU Timing Jitter
P4air needs μs-accurate timestamps
for RTT estimation.
BMv2 on VM CPU introduces random
delays → flow misclassification.
A CUBIC flow may be wrongly labelled
as delay-based (or vice versa).
2. Recirculation Bottleneck
Delay action uses recirculate() to
push packets back through pipeline.
On ASIC hardware: near-instant.
On BMv2 software: burns CPU cycles.
Throughput drops from 10 Mbps
to as low as 5.52 Mbps.
3. Scale Dependency
With only 4 flows across 8 queues,
hash-based separation works by luck.
Each flow lands in its own queue →
artificial fairness.
P4air's real advantage only shows
at 16+ flows (hash collisions).
Takeaway: Simpler dataplane logic can be MORE robust under software emulation constraints

## Slide 10
Our Proposal
Karma-Based Credit Scheduler
"Know if a flow is aggressive — not which CCA it runs"
10/22

## Slide 11
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
11/22
KBCS: Design Philosophy
Three guiding principles
1. Behavior Over Identity
Don't classify the CCA algorithm.
Just measure: is this flow sending
more than its fair share right now?
→ Simpler logic, fewer registers
→ No RTT estimation needed
→ No recirculation required
2. Fast Penalty, Slow Recovery
Aggressive flows lose karma quickly.
Well-behaved flows regain trust slowly.
Penalty: –5 per aggressive packet
Reward: +1 per compliant packet
→ Asymmetry prevents oscillation
→ Stabilizes queue behavior
3. Queue-Based Enforcement
Map karma to priority queues:
GREEN (K>80) → High priority
YELLOW (40<K≤80) → Medium
RED (K≤40) → Low / Drop
→ Protects well-behaved flows
→ Forces aggressors to slow down
P4air asks: "What CCA is this flow running?" → KBCS asks: "Is this flow being greedy?"

## Slide 12
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
12/22
The Karma Algorithm
What happens when a packet arrives at the switch
Step 1: Flow Identification
Hash the 5-tuple (src/dst IP, ports, protocol) using CRC16 → flow_id indexes into 65,536-entry register array
Step 2: Decayed Byte Estimation
flow_bytes = (flow_bytes >> 1) + packet_length → EWMA approximation using only bit-shift (no floating point, no timers)
Step 3: Karma Update
If flow_bytes > threshold → Karma -= 5 (penalty) If flow_bytes ≤ threshold → Karma += 1 (reward) Clamp to range [0, 100]
Step 4: Color Classification
K > 80 → GREEN | 40 < K ≤ 80 → YELLOW | K ≤ 40 → RED
Step 5: Queue Mapping + AQM
GREEN→ high-priority queue | YELLOW→ medium | RED→ low / drop

## Slide 13
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
13/22
Karma State Transitions
Fast penalty, slow recovery — visualized
GREEN
K > 80
High Priority
YELLOW
40 < K ≤ 80
Medium Priority
RED
K ≤ 40
Low / Drop
──── Aggressive (K -= 5) ────▶
──── Aggressive (K -= 5) ────▶
◀──── Compliant (K += 1) ────
◀──── Compliant (K += 1) ────
↓ New Flow (K = 100)
Recovery math: RED → YELLOW requires 40+ consecutive compliant packets
YELLOW → GREEN requires another 20+ compliant packets. This asymmetry prevents oscillation.

## Slide 14
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
14/22
KBCS Processing Pipeline
End-to-end packet flow through the programmable switch
Senders
h1: CUBIC h2: BBR (100 Mbps each)
▶
Parser & 5-Tuple Hash
Extract headers CRC16 → flow_id (65K register array)
▶
Decayed Byte Tracking
flow_bytes = (old >> 1) + pkt_len (EWMA, no timer)
▶
Karma Update
Aggressive? K -= 5 Compliant? K += 1 Clamp [0,100]
▶
Flow Color & Queue Map
GREEN → Q_high YELLOW → Q_med RED → Q_low/Drop
▶
Bottleneck + Receiver
10 Mbps link 5ms delay → h3 receiver
Key Advantage Over P4air
• Only 2 registers per flow (vs. 13+ for P4air)
• Zero recirculation (no CPU overhead in BMv2)
• No timer dependency (decay happens on packet arrival)
• O(1) per-packet processing (constant-time lookup and update)

## Slide 15
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
15/22
Feedback Loop: How Senders React
KBCS influences senders through standard TCP congestion signals
CUBIC (Loss-Based — The Aggressor)
KBCS drops packets when Karma ≤ 40 (RED)
CUBIC detects loss via duplicate ACKs
→ Performs multiplicative decrease
→ Cuts CWND by ~30%
This IS the intended behavior.
KBCS forces CUBIC to see the congestion
it's causing.
BBR (Model-Based — The Prober)
KBCS places low-karma BBR flows in
lower-priority queues → increased RTT
BBR observes increased RTT
→ Adjusts pacing rate downward
Queue-based delay is MORE effective
for BBR than packet drops, since BBR
deliberately ignores isolated losses.
Vegas (Delay-Based — The Victim)
Vegas naturally backs off when RTT rises.
KBCS PROTECTS Vegas flows:
→ They stay GREEN (high karma)
→ High-priority queue
→ Minimal queuing delay
Result: Vegas gets fair bandwidth share
instead of being starved.

## Slide 16
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
16/22
P4air vs KBCS: Side-by-Side
Precision vs. simplicity tradeoff
Aspect | P4air | KBCS
Decision Basis | Full CCA fingerprinting | Behavior-based karma score
State Per Flow | 13+ registers | 2 registers (bytes, karma)
Classification | 4 CCA groups + lifecycle | 3 colors (GREEN/YELLOW/RED)
Penalty Type | CCA-specific (drop/delay/halve) | Uniform karma degradation
Recovery | Implicit (reclassification) | Explicit (+1 per packet)
Recirculation | Required | Not needed
Timer Dependency | Critical (RTT estimation) | None (packet-driven decay)
BMv2 Robustness | High variance (σ = ±1.61 Mbps) | Expected lower variance

## Slide 17
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
17/22
What's Built So Far
Current repository status at mid-semester
✓
P4air baseline: implemented & multi-run evaluated (30-run + 16-flow)
✓
KBCS design documents & SRS: comprehensive specifications complete
✓
KBCS P4 prototype: parser, hash, byte decay, karma update, color mapping
✓
Plain forwarding baseline: separate P4 program for direct comparison
✓
Mininet topology: h1(CUBIC) + h2(BBR) → s1 → h3, 10 Mbps bottleneck
✓
Experiment automation: run_experiment.py driver with iperf3 integration
○
Priority-queue integration in main experiment flow
○
Queue-depth-aware KBCS decision logic
○
Comprehensive KBCS vs baseline result archive
○
Final parameter tuning & analysis
COMPLETED
IN PROGRESS / PENDING

## Slide 18
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
18/22
KBCS Prototype Parameters
Current values implemented in P4 code
Parameter | Value | Purpose
Register Size | 65,536 | Max concurrent flows (CRC16 hash space)
Initial Karma | 100 | All flows start fully trusted
Penalty Step | –5 | Fast punishment for aggressive sending
Reward Step | +1 | Gradual trust recovery
High Threshold (K) | 80 | GREEN boundary
Low Threshold (K) | 40 | RED boundary
Byte Threshold (θ) | 120,000 bytes | Aggressiveness detection level
Decay Formula | bytes = (bytes >> 1) + pkt_len | EWMA via bit-shift (50% decay)
Design Gap — Honest Assessment
Current prototype ≠ full enhanced design target.
• Queue-depth-aware decision logic → not yet integrated
• Selective AQM (drop only critical RED) → current code
drops all RED packets immediately
• Priority queue flag → not passed consistently in
experiment runner
This is acknowledged and planned for Phase 2.

## Slide 19
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
19/22
Baseline Evaluation Results
Measured, reproducible, already in the repository
30-Run Average (4 flows: CUBIC + BBR + Vegas + Illinois)
Configuration | Avg Jain's FI | Avg Throughput | Std Dev (Mbps)
No AQM (FIFO) | 0.9672 | 9.81 Mbps | ± 0.27
Diff Queues (Hash) | 0.9541 | 10.02 Mbps | ± 0.43
P4air (CCA Aware) | 0.9452 | 9.68 Mbps | ± 1.61
16-Flow Scale Test (4× each CCA)
Configuration | Avg Jain's FI | Avg Throughput | Std Dev (Mbps)
No AQM (FIFO) | 0.9123 | 10.23 Mbps | ± 0.03
Diff Queues (Hash) | 0.9390 | 10.35 Mbps | ± 0.02
P4air (CCA Aware) | 0.9483 | 11.02 Mbps | ± 0.02
Key Observations
At 4 flows: FIFO appears fair (artifactual)
→ Lucky hash effect at small scale
→ P4air pays CPU cost for limited gain
At 16 flows: P4air truly shines
→ FIFO fairness drops (0.97 → 0.91)
→ P4air leads in both FI and throughput
P4air's variance is concerning:
σ = ±1.61 Mbps (recirculation cost)
→ KBCS aims for σ < ±0.5 Mbps

## Slide 20
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
20/22
KBCS Performance Targets
What we need to achieve for a credible evaluation
Target 1: Fairness
Jain's FI ≥ 0.95 at 16-flow scale
Must match or exceed FIFO (0.91)
and approach P4air (0.95)
Target 2: Utilization
Link utilization ≥ 90%
Fairness should not collapse throughput.
PFQ shows FI > 0.95 at U > 95% is possible.
Target 3: Stability
Throughput σ < ± 0.5 Mbps
P4air has σ = ± 1.61 Mbps in BMv2.
Simpler logic should be more stable.
Evaluation Methodology
• Dumbbell topology: 10 Mbps bottleneck, 5ms delay
• iperf3 traffic generation with controlled CCA mixtures
• Jain's Fairness Index: J = (Σxᵢ)² / (n · Σxᵢ²)
• 30+ repeated runs for statistical significance
• Compare: FIFO vs Diff Queues vs P4air vs KBCS

## Slide 21
KBCS: Karma-Based Credit Scheduler | Mid-Semester Presentation
21/22
End-Semester Roadmap
Four phases from prototype to final evaluation
Phase 1: Complete Queue-Aware Logic
• Integrate queue-depth-aware decisions
• Align parameters with enhanced design
• Selective AQM for RED flows
▶
Phase 2: Finalize Experiment Pipeline
• BMv2 priority queues in all KBCS runs
• Archive KBCS vs baseline results
• Automated plotting scripts
▶
Phase 3: Comparative Evaluation
• KBCS vs FIFO vs Hash vs P4air
• 30+ repeated runs per config
• Analysis: fairness, throughput, variance
▶
Phase 4: Final Report & Analysis
• Insert final KBCS result plots
• Sensitivity analysis (flow count, thresholds)
• Conclusions based on measured outcomes
Lessons Learned So Far
1. Evaluate at multiple traffic scales — small-scale results can be misleading
2. Complexity in BMv2 causes high variance — simpler can be better
3. A clean baseline is essential before claiming any improvement
4. Current prototype validates feasibility — full evaluation needs all phases

## Slide 22
Thank You
Questions & Discussion
Key Takeaways:
1. TCP fairness at the bottleneck is a real, measurable problem
2. P4 enables in-switch behavior tracking — we proved this with P4air baseline
3. KBCS's "know behavior, not CCA" approach = simpler & potentially more robust
4. Prototype working, baseline validated, end-semester evaluation planned
Gaurav Jaiswal · Ishan Chadha · Sameer Prasad | IIIT Allahabad | March 2026